## Slide 1: Multihopping in Wireless
IIIT Sri City
By
Dr. Hrishikesh Venkataraman

## Slide 2: Resource Allocation - Spatial Reuse and Interference
The State-of-the-art protocols provide a heuristic solution for
solving an NP-hard problem (optimum resource allocation)
These state-of-the-art mechanisms do not utilize the resources
efficiently.
An efficient resource allocation mechanism needs to benefit
from spatial reuse of resource and must outweigh the
drawbacks of increased interference.
A circular exclusion region of radius times the
transmission distance, is defined around every
communicating receiver.
Typically, protocol Interference model with = 2.0

## Slide 3
2 pairs can communicate simultaneously (both satisfy the Protocol Model)
2 pairs cannot communicate simultaneously
(only one of the pairs satisfy Protocol Model)
Interference Avoidance Model

## Slide 4
General Multihop Network

## Slide 5
The transmission distance of every communicating pair is
different and it depends on the topology and network density
The number of simultaneous communicating pairs, nt, for any
time instant, t, is a function of:
1. The distribution of mobile terminals,
2. The user density, and
3. The transmission distance’s and path losses of all concurrently
communicating pairs
Finding the maximum number of simultaneous pairs in a given coverage area is a very complex problem
No. of Concurrent Pairs

## Slide 6
General Scenario of Spatial Reuse
Notes: Determining the maximum number of simultaneous communicating pairs (where each pair has a different transmission distance) is a Non-deterministic Polynomial-time (NP)-hard problem.
Also, there is no central-entity

## Slide 7: System Complexity
Discrete optimization problem of NP-hard complexity
s is the side length of the coverage area,
xi and yi are the x and y-coordinate of the center of the exclusion range circle,
ri is the radius of the exclusion range circle

## Slide 8: NEXT Generation Wireless Network

## Slide 9: Single-hop TDMA System
TS i+1
TS i
TS i+2

## Slide 10: General Multihop System
TS i1
TS i
TS i2
TS i3
TSi = TSi1 + TSi2 + TSi3
Notes: The TSi is partitioned into 3 mini-slots. The single-hop link is split up into 3 hop link, such that, each of the multiple hops communicate over each of the mini TS.
It should be noted that, there is no spatial reuse of resources at this stage.

## Slide 11: Spatial Reuse in Multihop
TS i1
TS i2
TS i3

## Slide 12: Power Requirement
Multihop results in power reduction and provides benefit even without spatial reuse
P
Q
d
P
Q
d/
4
Y
X
Z
P
Q
Z
d/
2
d/
2
Single-hop and multiple hop transmission between P and Q
C1 = log2 (1 + 10(0.1γ1)),
where γ1 = PR − NO dB
PR = PT − LP1 dB
and
LP1 = k1 + 10α log10(d) dB

## Slide 13: Two-Hop Cellular System
dcn1
dcn2
relay

## Slide 14: State-of-the-Art Protocols for Two-Hop
dcn1 is distance between BS and relay node,
dcn2 is distance between relay node and MS,
N is the no. of possible routes between MS and BS,
rs is the selected route for the 2-hop transmission.
1. Shortest total distance (STD) selection scheme
3. Shortest relaying hop distance (SRD) selection scheme
2. Least longest hop (LLH) selection scheme

## Slide 15: Realistic Version of State-of-the-Art Protocols
1. Minimum total path loss (MTP) selection scheme
2. Least maximum path loss (LMP) selection scheme
3. Minimum relaying hop path loss (MRP) selection scheme
Considering a slow fading channel with a log normal shadowing
the relay selection scheme would be modified as:

## Slide 16: Cluster-based 2-Hop Design
The pairs located at diametrically opposite clusters communicate simultaneously.
Schematic Representation

## Slide 17
Synchronized Reuse Technique
SH: End-to-end communication of 2 links in 1 TS
CBD-TH: End-to-end communication of 2 links (4 pairs) in 2 TSs
Same amount of radio resource as in single-hop communication

## Slide 18: Communication Principle
End-to-end (BS to MS)
communication within
same TS
Same radio resource
reused across every
cell
Frequency reuse of
one
Notes: There are 4 cases:
2 in Uplink and
2 in Downlink

## Slide 19: Deterministic Cluster-based Design
Cell 0
Cell 1
Cell 1
Cell 0
r/2
r/2
r/2
r/2
r/2

## Slide 20: Interference Distance Calculation
Downlink, BS to GTW communication
Downlink, GTW to MS communication
C/I at receiver of any communicating pair is given by:
The system capacity is calculated from the Shannon equation as:

## Slide 21
1000 MS(s) distributed within 19 cells
All communication in any cell takes place between MS and BS
Maximum number of hops between source and destination is 2
Interference calculation – from its own cell and 1st tier of cells
System capacity is calculated and averaged over 7 cells
Wireless nodes located between Tx and Rx are selected as relays
Simulation Parameters

## Slide 22
Gateway Selection

## Slide 23: Capacity Results - Downlink
Path-loss model remain the same for both single-hop and 2-hop model
2. Cluster-based design offers the maximum capacity for 2-hop cellular networks
3. σ = 4 dB.

## Slide 24: Capacity Results - Uplink
Cluster-based design aims for resource reuse in every cell.
This results in the highest system capacity as compared to other benchmark techniques.